Alignment Status and Commissioning Plans
Alignment Status and Commissioning Plans
Jim Pivarski, Alexei Safonov (Texas A&M)
Karoly Banicz (FNAL)

---
Alignment Needs
Alignment Needs
Physics analysis alignment (10/100 pb−1) :
  - Full procedure using large datasets
  - Necessary software tools
  - Full systematics studies
Validation:
  - Tests with real data to validate the procedure early
    - Cosmics, beam halo
  - Comparisons with other alignment information
    - Photogrammetry, optical, and hardware alignment
Commissioning(0-10 pb−1):
  - Procedure that uses minimal collisions data
    - Quick alignment of larger structures
    - Cosmics and beam halo for internal alignment measurements
    - Integration of other sources of alignment information (PG, HW)

---
Baseline Procedure
Baseline Procedure
Baseline procedure for physics quality datasets has been stable for some time
  - Based on the HIP algorithm
  - I Aligns one station at a time (from the inside out)
Hierarchical code structure matches system design
  - Fast alignment of large structures (~1000 muons)
  - Built-in support for constraints from prior knowledge
    - Photogrammetry, optical system
  - Capable of combining measurements from different sources
Optimization of parameters is in progress for faster convergence and better accuracy
  - Track-fitting parameters (APEs) tuned for each station
  - Intelligent track selection to supress strongly scattering tracks
  - Optimized track-fitting to better use structure of the detector and material distribution (pending tests)

---
Improvements to Baseline Procedure
Improvements to Baseline Procedure
Illustration of improvements:
  - “Intelligent track selection” (MC, 100 pb−1)
Each line is a station’s resolution as a function of iteration
  - Improved alignment reaches 300 μm for inner stations (which drive momentum resolution)

---
Considerations for Early Commissioning
Considerations for Early Commissioning
Can’t accurately align all chambers with limited statistics
  - But can quickly align large structures if internal alignment is known from other sources
      - Although less important for momentum resolution in collision data
Track-based candidates:
Beam-halo or collision tracks passing through overlap regions - EMU
Cosmics for barrel
Non-track based:
Hardware alignment and photogrammetry very useful for cross-checks and filling in gaps
E.g. CSC z alignment, to which beam-halo is insensitive
Momentum resolution depends on absolute alignments, which are a combination of

---
Large Structure Alignment
Large Structure Alignment
Alignment of large structures weakly depends on internal misalignments:
For ~1 mm chamber misalignments:
  - RMSx,y~0.6 mm, RMSz~3 mm, RMSz~ 0.1 mrad
Tracker misalignment is negligible for such large solid angles

---
Commissioning Plan
Commissioning Plan
CRAFT Tracker to Chamber Alignment (May):
    - Near-IP Muons: ~1M in Barrel 0, ~10k in ME1/3
  - Validation of the baseline procedure
    - Sanity checks: residuals for tracker muons
  - Comparisons with PG and HW alignment (ME1/3 & barrel)
    - Exercise use of HW and PG as constraints
Beam halo internal ring alignment (June):
  - Re-configured baseline procedure
  - Similarly, cosmics could be used for Barrel
Collisions (July?):
  - Ring alignment using internal alignment results
    - Similarly, we will align wheels if internal alignment available
  - Overlap tracks to cross-check internal alignment
  - Comparisons with PG and HW alignment
  - Use of PG and HW as constraints in baseline procedure
Next few slides provide details of the implementation

---
Internal Alignment with Beam Halo
Internal Alignment with Beam Halo
No collisions alignment:
  - Beam-halo through overlap regions (no ME1/3)
Few-collisions alignment
  - Align rings relative to tracker with ~1000 GlobalMuons
  - Complements beam-halo for a complete alignment
Minimal track propagation, measure x,y,y,z
Beam-halo rate hard to predict
With sufficient rate, good for layer alignment
Chambers are aligned relative to one another within each ring
Chambers misaligned within ring, ring position unknown
Chambers aligned within ring, ring position unknown
Chambers aligned within ring, ring position known

---
Internal Alignment with Beam Halo
CSC chambers in the same ring overlap
  - Easy to align w.r.t. each other using tracks passing through overlap regions
Algorithm:
  - Alternate and repeat, iterate
Will be done in the same framework
  - Re-configured for local alignments
Tightly refit tracks to even-numbered chambers
Loosely fit to odd-numbered to get local extrapolation from even to odd

---
Beam Halo Rate
Beam Halo Rate
Beam halo rate is 6600 tracks/sec (known up to a factor of 100)
Rate of overlap tracks 6600 × 0.02 = 130 Hz
  - 2 hours to collect 1M muons
Means 100’s of μm resolution
8 days if we’re off by ×100
Steeply falling function of energy and radius (better for internal rings)
(K. Banicz)
Trigger proposed, HLT path is being defined now

---
Alignment Framework Status
Alignment Framework Status
Recent progress
  - Parallelized 10/100 pb−1 procedure
  - Added CSCRing as an alignable structure
  - Tool for setting arbitrary patterns of hit weights (APEs)
  - Improved track cut and alternate refitter for upcoming tests
  - Mechanism for setting global coordinate system
  - HLT paths and AlCa streams for beam-halo, cosmics
  - Beam-halo and cosmic MC production cfg
  - DB interface with human-editable files and monitoring plots – ½ done
Procedure status
  - 10/100 pb−1 GlobalMuons: baseline working, can be optimized further, studied in more detail
  - Cosmic ray version of high-lumi GlobalMuons: need MC
  - Beam-halo: procedure designed, being implemented
  - 1000 muon ring alignment: easy adaptation of GlobalMuon

---
Datasets and Procedures
Datasets and Procedures
Single Muon trigger will be evolving with time
All Muons stream will be selecting all of these:
  - Cosmic rays during CRAFT
  - Very loose muons (single LCT) during commissioning
  - Good muons in long term
Overlap muon samples will have to be split by station
AlCa cuts will start loose and will evolve with time
  - Additional selections for now will be applied downstream
?
5 GeV in CSC and overlap on track
5 GeV in CSC
5 GeV in CSC and overlap on track
10 GeV
AlCa Cuts
Even-odd procedure (relative chamber alignment within ring)
(Non-iso OR iso) AND overlap
Beam-halo
Beam-halo in CSC overlaps
Baseline tracker-to-chamber (absolute chamber positions);
Structure Alignment;
Layer alignment procedure
(Non-iso OR iso)
Single-muon
“All Muons”
Internal barrel alignment?
(Non-iso OR iso)
RBC
Dedicated Cosmics
Beam-halo
Single-muon
L1
Layer alignment procedure
(Non-iso OR iso)
All Beam-halo
Even-odd procedure (relative chamber alignment within ring)
(Non-iso OR iso) AND overlap
Muons in CSC overlap
Procedure
HLT
AlCa Streams

---
Pre-Requisites for PG and HW Comparisons
Pre-Requisites for PG and HW Comparisons
Results of HW and PG have to be in the standard form to be able to do comparisons
Specific requirements:
  - Format of measurements (HW and PG):
    - Layer positions corrected for shifts (Oleg’s calculations)
    - Chamber positions must be defined as average position of layers (accounted for shifts)
    - CSCAlignmentRcd, DTAlignmentRcd delivered to Conditions DB
We propose to make comparisons of alignment measurements during these periods:
  - CRAFT, Beam halo data taking, Collisions
  - Results of HW alignment measurements have to be uploaded to Conditions DB to make comparisons

---
Possible Comparisons with HW and PG
Possible Comparisons with HW and PG
CRAFT Period Comparisons with HW:
  - A direct comparison of chamber positions in global coordinates, as reported by HW alignment and track-based system using DB Comparison tool
  - Effectively a test of the HW alignment in the barrel from chambers to tracker through the Link System
  - Pre-requisite: HW alignment results have to be propagated down to layer positions
    - Actually, that’s what AlignmentRcd holds
PG measurements:
  - Some sort of fitting will be needed: fit the two geometries for compatibility up to a rotation and translation
    - Accounts for PG (0,0,0) not being on tracker (0,0,0)

---
Possible Comparisons with HW and PG
Beam Halo Period:
Verification of relative chamber positions on each CSC ring
  - Beam-halo measures x and y positions
  - HW measures x (and z) with SLM lines
  - Will use the same fit method to check compatibility of x-measurements
Comparison with PG:
  - Fit to check compatibility of x- and y-measurements of chamber positions on the ring

---
Possible Comparisons with HW and PG
Collisions Data (first ~1000 muons):
Comparison with HW alignment:
  - Assuming completed inner alignment measured with beam halo, we have full alignment (down to chambers), so does HW
  - A direct comparison of chamber positions (defined as average layer positions) with the DB Comparison tool
Comparison with PG:

---
Suggested alignment scenarios
Suggested alignment scenarios
Chamber/Ring/Disk (C/R/D)
0 pb−1 beam-halo plus HW measurements
x	y	z	x	y	z
C	700 μm	2 mm	3 mm	3 mrad	0.8 mrad 0.65 mrad
R	200 μm	200 μm	230 μm	0.08 mrad 0.08 mrad 0.03 mrad
D	200 μm	200 μm	3 mm	1 mrad 1 mrad 0.03 mrad
1 pb−1 beam-halo plus GlobalMuon ring
x	y	z	x y	z
C	700 μm	2 mm	3 mm	3 mrad	0.8 mrad 0.65 mrad
R	600 μm	600 μm	3 mm	1 mrad	1 mrad	0.1 mrad
10 and 100 pb−1 track-based (without improvements)
x	y	z	x y	z
C	700 μm	2 mm	3 mm	3 mrad	0.8 mrad 0.65 mrad

---
Conclusions
Conclusions
Muon track based alignment system is functional:
  - Flexible to allow relative (local on structures) and global (w.r.t. tracker) alignment due to hierarchical structure reflecting design of the muon system
  - Ability to incorporate external alignment information in a consistent fashion as constraints or initial alignment
  - When recent improvements included, expected to reach design accuracy with 100 pb-1, further optimization ongoing
Updated alignment scenarios are conservative
  - Do not include recent improvements
Presented commissioning plan makes best use of information as it becomes available

---
Startup Luminosities
Startup Luminosities
Startup Luminosities
Each step lasts ~ 1 week
3.9
1.9
0.38
0.76
0.21
0.05
Low
Pileup
20 minutes
39 minutes
3.3 hours
5.9 hours
21 hours
4.0 days
4.1 years
Time for 1000 muons
3.8 x 1029
3 x 1010
18
43 x 43
1.7 x 1030
3 x 1010
4
43 x 43
6.1 x 1030
4 x 1010
2
43 x 43
1.1 x 1031
4 x 1010
4
156 x 156
 5.6 x1031
9 x 1010
4
156 x 156
1.1 x1032
9 x 1010
2
156 x 156
1027
1010
18
1 x 1
Luminosity
Ib
*
Bunches